## Slide 1: Service and Diagnostics on the DL2 Doppler speedlog
The most common reported faults
The analysis tools
How to use the tools
Logging
Service software
Built in test equipment
How to tackle a service
Remote login
The most common service tasks

## Slide 2: Service and Diagnostics DL2
First task is to find out which part of the system is having issues
  User interaction (Calibration, deeper settings)
    (photos or download of settings, software versions)
  Electronic hardware
    (Quality (noise) levels and signal output, internal tests or from logged files)
  Wiring
    (noise levels, signal strength)
  Sensor
    (noise levels signal strength , use of internal BITE and ETT tester)
  Mounting
  (analysis of files while vessel is moving and manouvring)

## Slide 3
The analysis tools
Built in test equipment
  Communication check
  Live Signal monitoring
  Raw data logging
Logging
  Inserting the USB stick will trigger logging of settings, results and ancilliary inputs. This allows post processing and analysis
Service software / analysis tools
  Logged data can be retrieved, viewed and analysed within these tools
  Software versions can be updated within these tools
Remote diagnostic support
  Using anydesk or teamviewer on a internet activated service PC, the system can be operated remotely, using the above tools to diagnose, download data, and adjust the system

## Slide 4: www.skipper.no
The analysis tools, and softwares, can be freely downloaded from the SKIPPER download pages

## Slide 5: Service and Diagnostics
Checking the status of the sensor
Sensor live
  Speeds at different frequencies
  Quality of the signals >3
  Depth is near correct?
Self test (demo)

## Slide 6: Service and Diagnostics
Raw Data
  Insert USB stick
  Raw Data type - Select the channel that is failing most
  Raw data band – select the frequency you wish to check for
    STW default high
    SOG default low
  Log Raw Data - Start logging
  This function takes a longer time to communicate, so once running, do not press the buttons fast.
  If all fails, restart the system
  Log for at least a minute, and best at the time you are hving the problems
Analyse the data on the USB stick using service software or analysis software

## Slide 7: Service and Diagnostics
Looking at the logged data
  USB stick will contain a directory SKIPPER, and a number of files
Analyse the data on the USB stick using service software or analysis software (demo)

## Slide 8: Service and Diagnostics
  Looking at raw data (demo)
  Service software
  - Shows frequency signal, if they are too weak, no speed detected

## Slide 9: Service Equipment
Voltmeter
Echo sounder and NMEA adapter
PC with ethernet and SKIPPER software

## Slide 10: When service is requested
Before service visit get:
Serial number of unit – Check no known issues with that unit.
Software versions in use. (config – JB70 setup / Screen setup)
Fault description
Photo/print out of «echo scope» when problem occurs
Customer to insert a USB stick
If necessary set up a remote session

## Slide 11: When service is requested
On receiveing data
Serial number of unit – Check no known issues with that unit.
Check the software is recent, check the change descriptions to see if this issue is tackled.
Look at data, verify the issue
Categorise the issue, sensor, electronics, software
Check SKIPPER diagnostics for solutions, failures, data bullitins, software updates

## Slide 12
REMOTE Access
This method requires a Windows computer/laptop and an ethernet cable connected directly to a free ethernet port of the system being accessed – this is the recommended connection.
Some software is required to support a remote access. Please download and install the below software:
Install Skipper Service software “SetupProjectServiceSoftware.msi” (LINK to WEB)
Install Remote Desktop Client – AnyDesk (LINK to WEB)
Download the latest SW version SW-M007, the same version of “ESN100 PC version for windows” and “ESNdrivers windows.rar” to your Desktop (LINK to WEB)
Two connections from your computer are required. We recommend using your WiFi adapter as a connection to internet (WiFi Network, 4G Dongle or through your mobil/cell – phone) and your ethernet adapter as a direct connection to the system being accessed.

## Slide 13
ESN REMOTE Access
Preconfigure your computer ethernet adapter to be on same sub net as the system being accessed, (default is 172.16.1.xxx) e.g. 172.16.1.50 (static) following below configuration:
How to set a static IP address in Windows
Click Start Menu > Control Panel > Network and Sharing Center or Network and Internet > Network and Sharing Center.
Click Change adapter settings.
Right-click on Local Area Connection.
Click Properties.
Select Internet Protocol Version 4 (TCP/IPv4).
Click Properties.
Select Use the following IP address.

## Slide 14
ESN100 REMOTE Access
When ready please share your Access Code for remote access, depending on your configuration it may be required for you to accept an incoming remote access request by SKIPPER Service.
When session is finished you may disconnect ethernet cable and reset your computer ethernet adapter settings to obtain and IP address automatically.

## Slide 15: Known systems faults
Sensor stops communicating
Sensor gives poor data or looses bottom
Failure during software update, system wont start
Self test fails
Older issues
False - No communication alarms
Failure during Sensor firmware update
General Multi issues
- Touch functionality defective. – Touch calibration
- Black screen – Dimming too low
-

## Slide 16: Sensor stops communicating
  Most likely issue
    Cabling failure
    If sensor is installed before oct 2020, could be a sensor oscillator failure
    If installed after, contact SKIPPER
  Things to test
    Is this a new installation, check the cabling, there are multiple blue and green cables. Make sure this is correct
    If previously working, check cabling
    Check ‘Fit check’
    Did this happen during upgrade? Check you cannot program the system, try programming from the connection box
      Program directly from the Service software
  If all fails check with SKIPPER / change the sensor.

## Slide 17: Sensor gives poor data
  Most likely issue
    Sensor has bubbles
  Things to check
    Has the sensor been cleaned
    Did it ever work (if not check mounting)
    Is the sensor properly seated in the valve
    Is all the wiring correct, and there is >21V at the connection box JB12/21?
    Get USB data and review/send to SKIPPER for review
  Solutions
    Cleaning / reseating of the sensor
    Improvements in software/ Firmware

## Slide 18: Failure during software update
  Most likely issue
    Interuption during upgrade
  What to check
    Can you search the system? Yes – Try a new upgrade
    if not Can you ping the system? In search type ‘cmd’, and then ‘ping 171.16.1.101’
    If Yes, try a new upgrade using the IP number
    If the program will not start or screen keep crashing, try a full reset (you will lose you calibration)
    If you cant try deleting configs from service software

## Slide 19: Self test fails
  Most likely issue
    Poor communication to the sensor
  Further testing
    Check the wiring , has it ever worked?
    Check the serial number with SKIPPER, serials before S141235
  Solutions
  Poor wiring
  Possible sign of sensor failure is SN < S141235

## Slide 20: Remote login
  What can be done
    Run the display from a PC
    Update softwares
    By SKIPPER – check the filing system, configs
    By SKIPPER – Down load data from a usb stick

## Slide 21: Thats it!
  Thenk you for listening, A video of this session will be available on the SKIPPER web, later today.
  Remember, SKIPPER service are here for you, if you are having problems or just want us to check, make contact.
  www.skipper.no
  service@skipper.no
  Sales@skipper.no